## Slide 1: What Is Spectral Imaging? An Introduction
David Messinger, Ph.D.
Rochester Institute of Technology

## Slide 2: What is Spectral Imaging?
Over time (passive) imaging systems have improved their spectral (i.e., color) response, range, and sensitivity
  B&W (1 spectral band)
  Color (RGB, 3 spectral bands)
  “Multispectral” (typically a filtered or colored illumination system)
  “Hyperspectral” (use of a diffraction element such as a prism or grating)
Why more bands?
  more spectral information leads to greater material separability

## Slide 3: Basic Outline of Talk
Definitions: light, wavelength, and color
Overview of imaging systems
  What the camera sees
  How to collect color imagery
  Difference between multi- & hyperspectral
  Calibration, registration
Basic image processing concept
  Spatial processing
  Spectral processing
Questions

## Slide 4: Definitions
Wavelength: related to the energy of light and color; typically written as l

## Slide 5: Definitions
Color: optical property of materials; how it selectively reflects light
Reflectance: efficiency with which an object reflects light as a function of wavelength
Fluorescence: material property by which light is emitted at a different wavelength that it is illuminated with
Spectral band / channel: a specific color in an imaging system
Resolution: the projected area of each pixel on the detector onto the object
Spectral response: how sensitive the detector is to each wavelength of light

## Slide 6: Imaging System: What the Camera Sees
Table to hold object
light source
camera
Reflectance vs.
Transmission vs.
Fluorescence

## Slide 7: Imaging System: Your Cell Phone
Table to hold object
light source
camera
notional “Bayer” pattern for RGB digital camera
Placed in front of camera detector

## Slide 8: Imaging System: Filter Wheel
Table to hold object
light source
camera
Placed in front of camera and rotates

## Slide 9: Imaging System: Colored Illuminant
Table to hold object
color of light source is modified
camera
Must be done in the dark!

## Slide 10: Multi- vs. Hyper- Spectral
My definitions
MSI
  Spectral imaging system that uses filters or colored illumination
  Generally has 10’s of spectral bands without continuous spectral coverage
  Generally has higher spatial resolution
HSI
  Uses a dispersion element to project
  “rainbow” onto detector
  Either the object or the camera has to
  move
  Produces continuous spectrum per pixel
  Generally lower spatial resolution

## Slide 11: Basic Hyperspectral Imaging System
For spectroscopy, we need to spread the light out using a diffraction grating or a prism
Image is collected one line at a time, but full spectral information is collected for each line on 2D array
Second spatial dimension collected by platform or object motion
2D detector array
1D collection aperture

## Slide 12: Calibration
Camera records digital counts – raw data
Can be converted to radiance (physical units) with calibration coefficients
Can be converted to reflectance with known target in scene
Different from color balancing

## Slide 13: Image Registration
Two images of same object at different wavelengths but slightly offset
Images simply overlaid in pixel space
Images registered by content

## Slide 14: Spatial Image Processing
Uses information contained in the spatial domain
  Pixels are next to each other
Typically (but not always) done on a single band image
Examples
  Sharpening and filtering, attempting to remove blur
  Edge detection

## Slide 15: Spatial Image Processing
RGB from hyperspectral
PC band 1
High Pass Filtered

## Slide 16: Spectral Imaging Processing: Signatures
The actual measurement in each band
How “bright” is this object in this band relative to the other bands?
Useful for identifying bands of high contrast and for assessing spectral similarity

## Slide 17: Hyperspectral Pixel Signatures
Spectral measurement (reflectance) as a function of wavelength for three different materials

## Slide 18: Spectral Signatures in the Color Space
We think of pixels as points in a space where the axes are the various colors
Specific colors fall on the axes, mixtures fall in the space in between
Provides a mathematical description of the data that is useful
red
blue
green

## Slide 19: Principal Components Analysis (PCA
red
blue
As seen from the red axis: difficult to separate
As seen from the blue axis: difficult to separate
Consider this collection of pixels in two colors
They represent two different materials, but their color differences are subtle
Looking at them in either red or blue alone makes it difficult to distinguish

## Slide 20: Principal Components Analysis (PCA)
red
blue
new PCA axis 2
new PCA axis 1
Points are now easy to separate in PCA band 1
PCA provides a way to represent them with new axes
New axes are derived to maximize separation in first PCA dimension (band)
Now materials are easy to separate

## Slide 21: Principal Components Analysis (PCA)
What’s that weird plot ENVI gives me when I run PCA but before I see my result?
The “eigenvalues”: numbers that describe the amount of variability in each new band
When they go to zero there isn’t any more information contained
Related to the material diversity in the scene

## Slide 22: Spectral Similarity Measures
We measure how similar pixels are to each other based on their spectral similarity
Pixels of similar material will have similar spectral signatures
  And will appear of similar color in original image and in transformed images such as PCA
Spectral angle is one measure, but there are others
  In the case of spectral angle, smaller values indicate more similar

## Slide 23: Spectral Similarity Measures
red
blue
green
pixels treated as vectors in color space
red
blue
green
Angle between two vectors is a measure of color similarity

## Slide 24: Other tasks
Target detection
  “known signature detection”
  If I have an exemplar of what I’m looking for, assess how likely every other pixel is to be the same material
Anomaly detection
  Find pixels that are anomalous, or somehow different
Classification
  Label each pixel as belonging to one of n classes
  Can be done automatically or through training data

## Slide 25: Questions?
David Messinger
messinger@cis.rit.edu
https://xkcd.com/1688/